## Slide 1
2013-2022 Full Presentation
Orientation Packet
for those new to DPCAC Emissions Report
and a refresher for others
Fall 2024

## Slide 2
What’s in the Orientation Packet
Pounds
Emissions, Air Quality and Health 3
Why Review Emissions Reports 4
Where Emissions Come From 5
Where Data Come From 12
Where Numbers Come From 18
Acronyms, Terms, and Descriptions 26
For More Information 34

## Slide 3
Emissions, Air Quality and Health
Pounds
Emissions, Air Quality and Health
Emissions come from many sources, including industry
Minimizing emissions improves air quality, which is good for health and the environment
Report focuses on emissions from DPCAC plants
Other meetings may focus on air quality trends and on health data and research

## Slide 4
WHY EMISSIONS REPORTS?
Pounds
Learn what DPCAC plants release to air, land, and water
  Including pollutants contributing to ozone
Help public learn about chemicals in the community
Plants may learn from their own reports and others
Allows us to track trends, though trends are affected by changing circumstances
If you can measure it, you can manage it

## Slide 5: Where Emissions Come From

## Slide 6: Source of Air Pollution
All Air Pollutants
TCEQ Air Emissions Inventory (EI)
EPA
TRI-Air
Industry/ Plants
Transportation
Biogenic
Agriculture
Residential Heating & Cooking
Not to scale

## Slide 7
Two Kinds of Air Emissions
Pounds
Point sources
Fugitive sources- may occur at connections

## Slide 8
Point Source vs. Fugitive Emission Sources
Pounds
Point Source
Fugitive Emissions
CO
NOX
VOC
SOX
Gas Meter
13 fugitive sources

## Slide 9
Point Source vs. Fugitive Emission Sources
Pounds
Point Source
Fugitive Emissions

## Slide 10
Plant Sources of Air Emissions
Pounds
Boilers
Heaters
Cooling towers
Process vents
Tanks
Wastewater treatment
From:
Routine permitted activities, including maintenance startup, and shutdown
Loading and unloading of trucks and trains
Upsets
Spills
During:
NOx comes mostly from combustion in heaters and boilers.
VOCs come from many sources.

## Slide 11
Things DPCAC Plants Make or Do
That Generate Emissions
Pounds
Refine crude oil: PEMEX Deer Park
Manufacturer chemicals: Dow, Evonik, GEO, Lubrizol, NOVVI, OxyChem, Shell Deer Park Chemicals, Westlake Epoxy
Package and distribute lubricants: Valvoline
Store and ship other plants’ products: ITC, Vopak Exolum , Vopak Terminal Deer Park
Manage waste or wastewater from other plants: Clean Harbors, Texas Molecular

## Slide 12: Where Data Come From

## Slide 13
TCEQ Emissions Inventory
Reported annually by major sources to Texas Commission on Environmental Quality (TCEQ)
Just air -- all air releases of covered pollutants
2024 DPCAC Emissions Report Files
EPA Toxics Release Inventory
Reported annually to Environmental Protection Agency (EPA) by plants in certain kinds of business if plant has chemicals on TRI list above a set amount.
Releases to environment (air, land, water) and transfers off the plant site for further waste treatment and disposal

## Slide 14: Industry Reporting of Air Emissions
EPA Toxics Release Inventory (TRI-Air)
TCEQ Air Emissions Inventory (EI)
All Air Pollutants
(Point + Area + Mobile + Natural)
Not to scale
EI and TRI Overlap
14

## Slide 15
Comparing EI vs. TRI
Pounds
State requirements (TCEQ)
  Contaminants released to Air
  Required for permitting and compliance
  Almost all air contaminants (even small quantities)
Air Emissions Inventory (EI)
Federal Requirement (EPA)
  Contaminants released to air, water, and land
  Required for public right-to-know
  Approx. 820 chemicals that exceed specific thresholds
Toxics Release Inventory (TRI)
Both Reports
Include point source and fugitive emission values.
  Calculation methods including direct measurements, engineering estimates, and agency factors
  Include permitted and upset emissions
  Can show useful trends
  Small facilities are exempted

## Slide 16
Requirements for TCEQ EI Reporting
Pounds
A plant must submit an EI if it meets any one of the following
  Major Source
  In Harris County and emits at least 10 tons per year (TPY) VOCs, 25 TPY NOx, or 100 TPY of any other contaminant
  Emits more than 0.5 TPY of lead (Pb)
  Potential to emit 10 TYP of a single (25 TPY aggregate) hazardous air pollutant
  Subject to a special inventory

## Slide 17
Requirements for EPA TRI Reporting
Pounds
Plants must report if:
  the chemicals used in their processes are covered by the TRI program (approximately 820 chemicals)
  the plant makes more than 25,000 lbs. of a TRI chemical in a year
  the plant uses more than 10,000 lbs. of the TRI chemical in a year
  they have much smaller quantities of certain TRI chemicals

## Slide 18: Where Numbers Come From

## Slide 19
Where Numbers Come From
Pounds
Measurements from Continuous Emissions Monitoring Systems (CEMS), stack and vent tests, lab analysis, and other direct measurements
Estimates from calculations based on fuel consumption, mass balance of process, engineering calculations, throughput formulas, flow measurements, inventory loss, production data, and field surveys
  Fugitives often estimated by EPA’s AP-42 factors
  Direct measurements may be incorporated into calculations
Changing calculation methods
  Improves accuracy
  Affects emissions numbers positively or negatively

## Slide 20: Measurements Continuous Emission Monitoring System (CEMS)
Most accurate way to quantify emissions
….and the most expensive to install & maintain
Only available for certain kinds of emissions
20

## Slide 21: Emissions Measurement Example
NOx emissions calculations basis
    NOx and CO CEMS data (concentration, ppmvd)
    Exhaust gas flow rate (dscfm)
    Molecular weight (lb/lb-mol)
  Boiler NOx example:
C ppmvd * MW lb/lb-mol * Q dscfm * 60 min/hr = lb/hr
Videal gas, cf/lb-mol * 106
  17.86 * 46.1 * 19,150 * 60 = 2.45 lb/hr NOx
386.5 * 106

## Slide 22: Measurement + Calculation
Fugitive VOC emissions calculation basis
    EPA Test Method 21 monitoring results
    EPA/TCEQ correlation equations
    Annual Leak Report

## Slide 23: Published Emission Factors
Emission factors are continuously revised and added!

## Slide 24: Emission Factor Example

## Slide 25: Factors Causing Year-to-Year Variations
Actual long-term changes in emissions
  Plant or unit start-ups or shutdowns
  Pollution prevention efforts – practices/equipment
Making different products from year to year
Production/customer demand - up or down
Maintenance and related shutdowns and startups
Changing number of plants in DPCAC
Changing calculation methods
Upsets, leaks and spills
Weather

## Slide 26
Emissions and Air Monitoring Acronyms and Terms

## Slide 27
Common Acronyms
Pounds
EPA – US Environmental Protection Agency
TCEQ – Texas Commission on Environmental Quality
Agencies
NOx –Nitrogen Oxides
VOCs – Volatile Organic Compounds
HRVOC – Highly Reactive Volatile Organic Compounds
SOx –Sulfur Oxides
TSP – Total Suspended Particulates
CO – Carbon monoxide
Criteria Pollutants/ Precursors
Inventories
EI – TCEQ Air Emissions Inventory
TRI – EPA Toxics Release Inventory
Other
TAR – Turnaround
HYCO – Hydrogen, Carbon Monoxide (components of Syngas)

## Slide 28
EI- Emissions Inventory filed with TCEQ for all criteria pollutants (and their precursors) and hazardous air pollutants, such as benzene and 1,3-butadiene.
TRI- Toxics Release Inventory, filed with EPA
Emission: Pollution discharged into the atmosphere from smokestacks, other vents, and surface areas of commercial or industrial facilities; from residential chimneys; and from motor vehicle, locomotive, or aircraft exhausts. (EPA)
Release- Any spilling, leaking, pumping, pouring, emitting, emptying, discharging, injecting, escaping, leaching, dumping, or disposing into the environment of a hazardous or toxic chemical or extremely hazardous substance. (EPA)
Environment- Air, water, groundwater, and land.
Emissions & Air Monitoring Acronyms & Terms

## Slide 29
LDAR- Leak Detection and Repair. Fugitive emissions are controlled by looking for leaks and fixing them. See gas meter (fugitives) vs. hot water heater (point sources).
DOR- Delay of Repair is a common cause of fugitive emission increases when leaking component cannot be repaired without shutting down plant. More emissions would result from the shutdown than from delaying repair. Components can also placed on DOR if it would be unsafe to attempt repair with chemicals in the process piping or equipment.
TPY- Tons Per Year
Emissions & Air Monitoring Acronyms & Terms

## Slide 30
Ozone- Respiratory irritant that may form in the atmosphere when NOx and VOCs come together on still, sunny days.
NOx- Nitrogen Oxides. Nitrogen dioxide and other gases made of varying mixtures of nitrogen and oxygen. Formed when fuel is burned at high temperatures. (EPA)
VOCs- Volatile Organic Compounds. Volatiles evaporate rapidly. Organic Chemicals or Compounds are naturally occurring (animal or plant-produced) or synthetic substances containing mainly carbon, hydrogen, nitrogen, and oxygen. VOCs are any organic compounds that participate in atmospheric photochemical reactions except those designated by EPA as having negligible photochemical reactivity. (EPA). Photochemical reactions are influenced or initiated by light. There are hundreds of VOCs, including common ones like ethylene, propylene, benzene, and formaldehyde. VOCs are found in many household products and are thus an indoor air quality interest.
FGRS- flare gas recovery system
MSS- maintenance, shut down and startup
RTO- regenerative thermal oxidizer to reduce emissions to the atmosphere
TO- thermal oxidizer
WWT- wastewater treatment
WWTP- wastewater treatment plant
Emissions & Air Monitoring Acronyms & Terms
Criteria Pollutants and Precursors

## Slide 31
CO- Carbon Monoxide. Formed when fuel is not burned completely.
TSP- Total Suspended Particulates. Mixture of solid particles and liquid drops found in the air. Some particles, such as dust, dirt, soot, or smoke, are large or dark enough to be seen with the naked eye. Others are so small; they can only be detected using a microscope.
SOx - Sulfur Oxides (including sulfur dioxide and others in the family). Sulfur is prevalent in crude oil, coal, and ore that contains common metals like aluminum, copper, zinc, lead, and iron. SOx gases are formed when fuel containing sulfur, such as coal and oil, is burned; when gasoline is extracted from oil; or metals are extracted from ore.
Emissions & Air Monitoring Acronyms & Terms
Criteria Pollutants and Precursors

## Slide 32
Benzene- a colorless liquid with a sweet odor. It evaporates into the air very quickly and dissolves slightly in water. It is highly flammable and is formed from both natural processes and human activities. Benzene is widely used in the United States; it ranks in the top 20 chemicals for production volume. Some industries use Benzene to make other chemicals that are used to make plastics, resins, nylon, and other synthetic fibers. Benzene is also used to make some types of rubbers, lubricants, dyes, detergents, drugs, and pesticides. Natural sources of Benzene include emissions from volcanoes and forest fires. Benzene is also a natural part of crude oil, gasoline, and cigarette smoke. It is a known human carcinogen. (Source: Agency for Toxic Substances and Disease Registry)
Emissions & Air Monitoring Acronyms & Terms
Pollutant Descriptions

## Slide 33
1,3-Butadiene- a chemical made from the processing of petroleum. It is a colorless gas with a mild gasoline-like odor. About 60% of the manufactured 1,3-Butadiene is used to make synthetic rubber. Synthetic rubber is widely used for tires on cars and trucks. 1,3-Butadiene is also used to make plastics including acrylics. Small amounts are found in gasoline. It is a carcinogen. (Source: Agency for Toxic Substances and Disease Registry)
Emissions & Air Monitoring Acronyms & Terms
Pollutant Descriptions

## Slide 34
TCEQ Home Page-
  www.tceq.Texas.gov
EPA
  TRI Program Home Page- www.epa.gov/tri
Houston Regional Monitoring:
  http://hrm.aecom.com
If You Want to Know More